## Slide 1: Biometric Recognition Lab Fingerprint Recognition
Kevin Hernández Díaz

## Slide 2: Fingerprint Recognition: Fingerprint Patterns
Fingerprints are composed of different patterns
  Parallel Lines
  Core points
  Delta points
  Minutia points

## Slide 3: Fingerprint Recognition: Fingerprint Patterns
Fingerprints are composed of different patterns
  Parallel Lines: Most common pattern in the fingerprint
  Core points
  Delta points
  Minutia points

## Slide 4: Fingerprint Recognition: Fingerprint Patterns
Fingerprints are composed of different patterns
  Parallel Lines
  Core points: 1-2 per fingerprint. ~180 direction change of the ridges in a local area
  Delta points
  Minutia points

## Slide 5: Fingerprint Recognition: Fingerprint Patterns
Fingerprints are composed of different patterns
  Parallel Lines
  Core points
  Delta points: 1-2 per fingerprint. Triangular shape pattern
  Minutia points

## Slide 6: Fingerprint Recognition: Fingerprint Patterns
Fingerprints are composed of different patterns
  Parallel Lines
  Core points
  Delta points
  Minutia points: Dozens per fingerprint. A point where a ridge ends or diverge in two/ two ridges converge in 1

## Slide 7: Fingerprint Recognition: brief reminder of complex numbers
In order to detect the feature points in a fingerprint we usually calculate the gradient image as done in the previous lab for edge detection
We can define this as a complex number if we consider the x axis to be the real part of the complex number and the y axis to be the imaginary part
Where i denotes the imaginary part

## Slide 8: Fingerprint Recognition: brief reminder of complex numbers
We can represent a complex number as a vector:
  With x (real) and y (imaginary) coordinates
  With magnitude and angle
Real
Im
(x,y)

## Slide 9: Fingerprint Recognition: brief reminder of complex numbers
We can represent the gradient image from the output of the derivative filter in each direction:
Real
Im
Real
Im
(Resx,Resy)
Resx
Resy
Euler identity

## Slide 10: Fingerprint Recognition: Detecting patterns in the image
From the gradient image we are interested in the “orientation map” which represents the local orientation at every pixel
We are not interested into exact pixel orientation but rather a local orientation
One problem arise, the gradient points into the direction of biggest change, so depending on which side of the ridge you stand, gradients points into opposite directions, which would make the local gradient=0!
ridges
valleys

## Slide 11: Fingerprint Recognition: Detecting patterns in the image
Solution?
  We multiply the angle at each pixel by 2!
ridges
valleys
ridges
valleys

## Slide 12: Fingerprint Recognition: Detecting patterns in the image
Detecting paraller lines:
Parallel line region
Gradient vectors
Core pattern region
Gradient vectors
Parallel line detector
Patterns
filters

## Slide 13: Fingerprint Recognition: Detecting patterns in the image
How do we calculate the scalar product between ”arrows”/vectors??
When calculating the scalar product with complex numbers, we conjugate the second vector
* Represents the conjugated
Real
Img
Complex vector
Real
Img
Complex vector
*
=
Real
Img
Complex vector

## Slide 14: Fingerprint Recognition: Detecting patterns in the image
Detecting paraller lines:
filters
Parallel line region
*
=
Core pattern region
filters
*
Long vector
Pointing at
1 direction
Null or small
vector

## Slide 15: Fingerprint Recognition: Detecting patterns in the image
Detecting core patterns:
Parallel line region
Gradient vectors
Core pattern region
Gradient vectors
Core detector
Patterns
filters

## Slide 16: Fingerprint Recognition: Detecting patterns in the image
Detecting paraller lines:
filters
Parallel line region
*
=
Core pattern region
filters
*
Null or small
vector
Core detector
Core detector
Long vector
With 90 degrees
orientation

## Slide 17: Fingerprint Recognition: Detecting patterns in the image
Conclusions:
 | Parallel pattern | Core pattern
Filter for lines | Long vector with same direction as pattern | Zero or null vector
Filter for cores | Zero or null vector | Long vector with orientation of 90 degrees

## Slide 18: Fingerprint Recognition: Detecting minutia points
Minutia points are located where a ridge ends or there is a bifurcation
Both can be detecting using the same filter since they have the same shape but oposite colors, so the gradients will be the same after the ”double” correction
Since minutia points ”look like” core-patterns we can use the same filter to detect them
Bifurcation
ending

## Slide 19: Fingerprint Recognition: Detecting minutia points
We will use both filters shown before to detect minutia points
Linear pattern filter:
  Long arrow in presence of parallel lines
  Small or null where there is a core-like pattern (minutia too)
Core pattern filter:
  Long arrow in presence of core pattern
  Small or null in regions where there is only parallel lines
Where C represents the output of the scalar prduct with the core filter and the L represents the output with the parallel filter
if we consider that C ~ 1 when there is a core pattern and ~ otherwise and L ~ 1 when it is a parallel lines regions and ~ 0 otherwise
with ~ 1 when in presence of a minutia point/core pattern
is to reinforce that in the presence of a minutia point the output for parallel lines should be close to 0

## Slide 20: Fingerprint Recognition: Pyramid detection
256x256
128x128
64x64
32x32
16x16
Level 0
Level 1
Level 2
Level 3
Level 4
We start from the full image at level 0, where all details are present.
  We can only detect minutia points at this level, since they are fine details in the image
We low-pass filter the image to remove details and then reduce the size by half
In higher levels only global/macro details are present (cores and deltas) and they are easier to detect
Once detected in a upper levels we can update their position in lower levels. More accurate than trying to directly detect them at level 0

## Slide 21: Fingerprint Recognition: summary of detection procedure
Cores/delta points:
  Core/delta points are available in all scales of the pyramid, thus find them in a higher level (e.g 3)
  Then go down to the lower scales and refine the position of the detected core/delta by looking around the position from the previous scale. Go until level 0 (highest resolution)
Minutia points:
  Minutia points are only available at lower scales, detect them at the highest resolution (scale 0)
  Minutia points are difficult to detect anyways if quality of the fingerprint is bad
  Then it may be necessary to enhance the image before the gradient is computed (will se in the lab exercise)